## Slide 1: Second Law of Thermodynamics
Why an Energy Balance is Not Enough

## Slide 2: Second Law
1st Law of Thermodynamics, can’t create or destroy energy
But why does heat only flow from hot areas to cooler areas?

## Slide 3: Second Law

## Slide 4: Second Law
Second law tells whether a process can take place
To do this need another property called entropy
Process can not take place unless it satisfies both first and second laws of thermodynamics

## Slide 5: Thermal Energy Reservoirs
Large body with extremely large thermal capacity which ca absorb or supply a finite amounts of heat with out changing temperature

## Slide 6: Thermal Energy Reservoirs
A reservoir that:
Supplies heat is a source
Absorbs heat is a sink

## Slide 7: Heat Engines
Work can be easily converted completely to heat and other forms of energy
Converting other forms of energy to work is not that easy

## Slide 8: Heat Engines
Work can be converted to work directly and completely
Converting heat to work requires the use of a device called a heat engine
Heat engines come in many forms, pure heat engines (steam power plants) and semi heat engines (gas turbines)
All have a working fluid

## Slide 9: Heat Engines
  Receive heat from high temperature source
  Convert part of the heat to work (usually a rotating shaft)
  Reject remaining waste heat to a low-temperature sink
  Operate on a cycle

## Slide 10: Heat Engines
Qin=amount of heat supplies to steam in boiler from high temperature source (furnace)
Qout=amount of heat rejected from steam in condenser to a low-temperature sink
Wout=amount of work delivered by steam as it expands in turbine
Win = amount of work required to compress water to boiler pressure
Wnet,out= Wout-Win (kJ)
Wnet,out= Qin-Qout (kJ)

## Slide 11: Thermal Efficiency
Thermal efficiency, ηth
ηth=net work output /total heat input
ηth = 1 – (heat out /total heat in)

## Slide 12: Thermal Efficiency
Spark-ignition engines turn 25% of chemical energy into mechanical energy
As high as 40% for diesel engines and large gas-turbine plants
As high as 60% for large combined gas-steam power plants

## Slide 14: 2nd Law of Thermodynamics
Kelvin-Planck Statement:
  It is impossible for any device that operates on a cycle to receive heat from a single reservoir and produce a net amount of work.
  No heat engine can have a thermal efficiency of 100%
  For a power plant to operate, the working fluid must exchange heat with the environment as well as the furnace

## Slide 15: Refrigerators and Heat Pumps
Heat moves in nature from high temperatures to lower temperatures, no devices required
The reverse process, heat from low temp to high temp, required special devices called refrigerators or heat pumps

## Slide 16: Refrigerators
Vapor-compression refrigeration cycle
Compressor
Condenser
Expansion valve
Evaporator

## Slide 17: Refrigerators

## Slide 18: Refrigerators
Coefficient of Performance (COP)
COP = Desired output/Required input
COPR = QL/Wnet,in = 1/((QH/QL)-1))

## Slide 19: Heat Pumps
Transfers heat from low temperature area to higher temperature area
COPHP = Desired output /Required input = QH/Wnet,in
COPHP = QH/(QH–QL) = 1/(1-(QL/QH))

## Slide 20: Energy Relationships
COPHP = COPR + 1
Energy efficiency rating (EER) amount of Btu removed per kWh consumed EER = 3.412 COPR
1 kWh = 3412 Btu

## Slide 21: 2nd Law: Clausius Statement
It is impossible to construct a device that operates in a cycle and produces no effect other that the transfer of heat from a lower-temperature body to a higher-temperature body

## Slide 22: Perpetual-Motion Machines
To take place, a process must satisfy both the first and second laws of Thermodynamics
A device that violates the 1st law (creates energy) is a perpetual-motion machine of the first kind (PMM1)
A device that violates the 2nd law is a perpetual-motion machine of the second kind (PMM2)

## Slide 23: PPM1

## Slide 24: PPM2

## Slide 25: Reversible Processes
If a heat engine can not be 100% efficient, how efficient can it be?
Answer lies in discussion of reversible processes
Reversible process is a process that can be reversed without leaving a trace on the surroundings

## Slide 26: Reversible Processes

## Slide 27: Reversible Processes
Reversible processes are idealized processes, do not occur in nature
Reversible processes are the “best” process that can be done
Irreversible processes are processes that are not reversible due to irreversibilities

## Slide 28: Irreversibilities
Irreversibilities are factor that cause processes to be irreversible
  Friction
  Unrestrained expansion of a gas
  Heat transfer

## Slide 29: Reversible Processes
Internally reversible: no irreversibilities within the boundaries of the system during the process. (quasi-equilibrium)
Externally reversible: no irreversibilities occur outside the system boundaries during the process. (heat transfer at same temperature)
Totally reversible: no irreversibilities within system or surroundings

## Slide 30: Reversible Processes

## Slide 31: Carnot Cycle
Ideal cycle, reversible
Four processes make up a cycle

## Slide 32: Carnot Cycle
Reversible isothermal expansion, TH = cont
Reversible adiabatic expansion, Q = 0
Reversible isothermal compression, TL = cont
Reversible adiabatic compression, Q = 0

## Slide 33: Carnot Cycle

## Slide 34: Carnot Cycle
Since a reversible cycle, reverse is a refrigeration cycle

## Slide 35: Carnot Principles
The efficiency of an irreversible heat engine is always less that the efficiency of a reversible heat engine operating between the same two reservoirs
The efficiency of all reversible heat engines operating between the same two reservoirs are the same

## Slide 36: Carnot Principles

## Slide 37: Carnot Heat Engine

## Slide 40: Quality of Energy
Energy has quality
More high-temperature energy can be converted to work
Higher the temperature, higher the quality

## Slide 41: Carnot Refrigerator and Heat Pump